## Slide 1: ◊ IoT Hands-on Labs ◊ Lab 4. ThingWorx
Prof. John Lee
IUPUI & KAIST
IoT Lecture Series

## Slide 2: ThingWorx Academic Tutorial
Follow tutorial here (on your own)
  https://www.udemy.com/thingworx-fundamentals/
Create an account on https://www.thingworxacademic.com/
  Registration Code: fundamentals17
  See next slide

## Slide 3
fundamentals17

## Slide 4: ThingWorx Academic Tutorial
Use the following composer for experiment
  (use same user ID and password as thingworxacademic.com)
  https://academic.cloud.thingworx.com/Thingworx/Composer/
We will do something very similar to this
  https://www.thingworx.com/ecosystem/academic-program/iot-projects/weather-app-arduino-uno/
Continue next slide

## Slide 5: ThingWorx Arduino Tutorial
use https://github.com/indystar1/ESP8266-code-various/REST_ESP8266_ThingWorx
If you have not downloaded the folder, clone or download
(Need Arduino IDE and ESP8266 library to program Wemos D1 ESP8266)
  we did this in earlier labs
Follow Lab_33.ThingWorx_experiment.pdf
  Create a Thing with five Properties: Temperature (Number), Humidity (Number), AnalogValue (Number), BoolStatus (Number), and MyControl (Boolean).

## Slide 6: ThingWorx Arduino Tutorial
Also create a Service whose name is setTempAndHumid with the following Script:
Continue next slide
me.Temperature = parseFloat(Temp) ;
me.Humidity = parseFloat(Humid) ;
me.BoolStatus = parseFloat(Bool) ;
me.AnalogValue = parseFloat(Analog) ;

## Slide 7: ThingWorx Arduino Tutorial
Use the same board we used in the previous lab
Modify REST_ESP8266_ThingWorx_JSON_LED_control.ino
  Modify the WiFi ssid, password, appKey, etc.
Connect power to the hardware.
Setup target board, port, speed, etc.
Compile
Upload to ESP8266

## Slide 8: Debugging (if it doesn’t work well)
Use Advanced REST client (chrome extension)
Command to use
  POST /Thingworx/Things/Your_Thing_Name/Services/setTempAndHumid?appKey=your_app_key&method=post&x-thingworx-session=true&Temp=56.70&Humid=34.50 HTTP/1.1
  Host: academic.cloud.thingworx.com
  Content-Type: text/html

## Slide 9: Mashup (GUI)
Next, create a Mashup like this:

## Slide 10: Mashup (GUI)
Launch the mashup and see if data change.
Try to turn Switch on and off
Try to cover photoresistor to see if Luminosity changes.
Now check or un-check LED on/off to see if LED2 on the board is turned on or off.