## Slide 1: ThingWorx Composer a web-based modeling & development environment
Prof. John Lee
IUPUI & KAIST
IoT Lecture Series

## Slide 2
Composer Home View

## Slide 3: GUI Composer 구성 요소들
Base Thing Template
Thing Template and Thing
Thing Shape
Value Stream or Data Stream
Event Notifier
Mashup (i.e., GUI or webpage) builder
AppKey
MailServer
Various SDKs
  C-SDK
  Java-SDK
Many extensions for various services, protocols, and devices
  ThingWorx Marketplace (http://marketplace.thingworx.com/)
http://support.ptc.com/cs/help/thingworx_hc/thingworx_6.0_hc/

## Slide 4: Terms
The Composer
  A web-based modeling and development environment
Thing (real)
  a device, physical asset, system or business process
  connected to the Internet
  An example: a portable weather station….
  In the Composer, a Thing is a data model (abstract) of a real thing.
    Something that takes in data and uses it to fire events, process services, etc. within the rest of the system based

## Slide 5: Base Thing Templates (page 1/3)

## Slide 6: Base Thing Templates (page 2/3)

## Slide 7: Base Thing Templates (page 3/3)

## Slide 8: Terms
Edge Micro Server (EMS)
  A device embeddable service (client code) providing a real time data channel to the ThingWorx server
  Available in C, Objective C, Java, and .NET versions
MashUps
  Web pages constructed with the Widgets that know how to connect with data on the ThingWorx server
Streams
  Fast data storage used to capture the Properties of your Things as they change over time.

## Slide 9: Terms
Tag
  A way for ThingWorx to identify (label) different elements (i.e. Thing Shapes, Things, etc.) as being part of the same project, which allows you to transfer projects across different servers

## Slide 10: Terms
Thing Shape
  Building blocks that can either go and build a template and then build a thing,
  or that can directly help you to build a thing
  tied to a project (tag)

## Slide 11: Terms
Thing Templates
  Like base classes in an object oriented language
  A way to combine shapes (multiple sources of data) that allows you to add additional property services, subscriptions, and events to create a unique template that allows for the rapid creation of any new thing
  tied to a project (tag)
  created based on a Base Thing Template
    e.g., RemoteThing (for receiving data remotely)
  may need Thing Shape
  may need Value Stream

## Slide 12: Creating a new Thing Template

## Slide 13: Additional Terms
Value Stream
Properties
Services
Events
Subscriptions

## Slide 14: Project Building Steps
Make your device and code its EMS details
  can use C-SDK, Java-SDK, etc.
Create an app-key
May creare ProjectName (an application name based on app-key): used as a tag
  only used for linking of things in one project
Create your Thing
  Base-Template  Thing Template  Thing
    Many Base-Templates are provided
  Thing Shapes

## Slide 15: Part of Device Source Code (EMS)
@ThingworxPropertyDefinitions(
properties = {
@ThingworxPropertyDefinition(
name = "Prop_Humidity",
description = "A Current humidity value from a AM2302 sensor.",
baseType = "NUMBER",
aspects = {
"dataChangeType:ALWAYS",
"dataChangeThreshold:0",
"cacheTime:0",
"isPersistent:FALSE",
"isReadOnly:TRUE",
"pushType:VALUE",
"defaultValue:0"
}
),
@ThingworxPropertyDefinition(
name = "Prop_Temperature",
description = "A Current temperature and humidity value from a DHT22 sensor.",
baseType = "NUMBER",
aspects = {
"dataChangeType:ALWAYS",
"dataChangeThreshold:0",
"cacheTime:0",
"isPersistent:FALSE",
"isReadOnly:TRUE",
"pushType:VALUE",
"defaultValue:0"
}
),
}
)

## Slide 16: Creating a Thing
Create based on a Thing Template
  If you don’t have (or don’t need) your own Thing Template, you can use GenericThing Template
Tied to a project (tag)
Users may want to create both a Thing Shape and a Thing Template that will define and house the Thing.
Notes: This will allow you to later utilize the data in a Mashup.

## Slide 17: Binding Data between a model Thing and real Thing
Need to create properties
  Names of properties must match with your sensor’s property names that you used when you implement your device
  Created within a Thing Shape or Thing Template
  Property types can be numbers, strings, Boolean, etc.
  Can also create alerts
    E.g., Humidity is higher than 60%

## Slide 18: Property Base Types

## Slide 19: Binding Data with a Thing
Within a Thing
  Bind the created properties with the data source (EMS side)
  At this moment in order for the ThingWorx to know data source with property names, the device should have already been connected to the server.
So, there should be a Monitoring window in the Composer
  displays connection status of devices
  see next slide

## Slide 20: Monitoring Window

## Slide 21: Thing Shape—Properties

## Slide 22: Thing Template—Properties
Modify alert

## Slide 23: Thing Template—Properties—Alert

## Slide 24: Value Stream (for sensor data streaming)

## Slide 25: Value Stream—Properties

## Slide 28: Value Stream—Events

## Slide 29: Thing—General Information

## Slide 30: Thing—Properties

## Slide 31: Thing—Services

## Slide 32: Thing—Events

## Slide 33: Thing—Subscriptions for events
Used to raise an alert while monitoring sensor data

## Slide 34: Event Notifier
Describe what to do for chosen events

## Slide 35: MailServer—Services
Can be used to send an email upon some events

## Slide 36: Mashup (Web Interface) Builder

## Slide 37: Web Interface (deployed)

## Slide 38: Various Widgets for Building Mashups (1/4)

## Slide 39: Various Widgets for Building Mashups (2/4)

## Slide 40: Various Widgets for Building Mashups (3/4)

## Slide 41: Various Widgets for Building Mashups (4/4)

## Slide 42: Configurable Properties of Google Map Widget

## Slide 43: Configurable Properties of Gauge Widget