## Slide 1: ◊ IoT Hands-on Labs ◊ Lab 4. ThingWorx
Prof. John Lee
IUPUI & KAIST
IoT Lecture Series

## Slide 2: ThingWorx Academic Tutorial
Follow tutorial here (on your own)
  https://www.udemy.com/thingworx-fundamentals/
Create an account on https://www.thingworxacademic.com/
  Registration Code: fundamentals17
  See next slide

## Slide 3
fundamentals17

## Slide 4: ThingWorx Academic Tutorial
Use the following composer for experiment
  (use same user ID and password as thingworxacademic.com)
  https://academic.cloud.thingworx.com/Thingworx/Composer/
We will do something very similar to this
  https://www.thingworx.com/ecosystem/academic-program/iot-projects/weather-app-arduino-uno/
Continue next slide

## Slide 5: ThingWorx Arduino Tutorial
use https://github.com/indystar1/ESP8266-code-various/REST_ESP8266_ThingWorx
If you have not downloaded the folder, clone or download
(Need Arduino IDE and ESP8266 library to program WeMos D1 ESP8266)
  we did this in earlier labs
Follow Lab_34.ThingWorx_experiment.pdf
  Create a Thing with five Properties: Temperature (Number), Humidity (Number), AnalogValue (Number), BoolStatus (Boolean), and MyControl (Boolean).

## Slide 6: ThingWorx Arduino Tutorial
Also create a Service whose name is setTempAndHumid with the following Script:
Continue next slide
var isTrueSet = (Bool.toLowerCase() === 'true');
me.Temperature = parseFloat(Temp) ;
me.Humidity = parseFloat(Humid) ;
me.BoolStatus = isTrueSet ;
me.AnalogValue = parseFloat(Analog) ;

## Slide 7: ThingWorx Arduino Tutorial
Use the same board we used in the previous lab
Modify REST_ESP8266_ThingWorx_JSON_LED_control.ino
  Modify the WiFi ssid, password, appKey, etc.
Connect power to the hardware.
Setup target board, port, speed, etc.
Compile
Upload to ESP8266

## Slide 8: Debugging (if it doesn’t work well)
Use Advanced REST client (chrome extension)
Command to use
  POST /Thingworx/Things/Your_Thing_Name/Services/setTempAndHumid?appKey=your_app_key&method=post&x-thingworx-session=true&Temp=56.70&Humid=34.50 HTTP/1.1
  Host: academic.cloud.thingworx.com
  Content-Type: text/html

## Slide 9: Mashup (GUI)
Next, create a Mashup like this:

## Slide 10: Mashup (GUI)
Launch the mashup and see if data change.
Try to turn Switch on and off and check Switch check box.
Try to cover photoresistor to see if Luminosity changes.
Now check or un-check LED on/off to see if LED2 on the board is turned on or off.

## Slide 11: Testing the Service
You could test your Service by clicking [Test] button in the Service entity.

## Slide 12: Service Testing Window
It will show the following Test Service Window, by which you can test your service.